## Slide 1: Sensitivity testing and coil design.
WEEK 7

## Slide 2: Lowest perceived field strength
With a 100Hz sine my lowest consistently perceived field:
< 0.005 mT*
*Reached the gaussmeter’s resolution limit (0.002mT) so we can’t be more precise.
In Harrison 2018, median at 200Hz :
0.03 mT
*Values were estimated from coil and signal, not measured...

## Slide 3
> 6 times more sensitive than expected, good but why?!
20% stronger implant
+
Measured values rather than estimated
(estimated ones seem to always be higher)
+
Parylene coating thinner than silicone (less useless mass)
+
Gaussmeter error? Waiting for the axial probe to arrive...

## Slide 4: Sensitivity in relation to frequency and signal type

## Slide 5
Each signal produces a different sensation. They can also be merged to extend the sensed frequency range.
100Hz was the most sensitive frequency despite being a blindspot for frequency discrimination (Harrison2018).
The most interesting range overall is 50-300 Hz with some interesting results on even lower frequencies.
Using lower frequencies I can produce a beating sensation (20-50 Hz) and a “deformation” sensation <20Hz (sine).

## Slide 6: Coil design
Usable range of a hand made ring coil of reasonable size : 3 cm*
Ideal usable range for a ring : +- 6cm **
*using optimized signal types for low frequencies
** ring around the base of proximal phalanx rather than medial

## Slide 7: Coil design
Increase width - impractical
Increase current - produces heat
Manage heat - impractical
Industrially made coils (+-30% more efficient, can fit more turns in less space)
Use a core

## Slide 8: Core designs
L core - 1.7x stronger field at 15mm No core

## Slide 9: Further thoughts
Stacking L-Cores?